Polytechnic University of Puerto Rico

Electrical Engineering Department

EE 5723     DSP Fundamentals Lab

Design Project      Spring Quarter 2003

Issued:  04/28/2003

Due: 05/24/2003

Late projects will not be accepted.

Maximum number of students per design team: 5

NAME _______________________________________________# ___________

NAME ______________________________________________# __________

NAME _______________________________________________# ___________

NAME ______________________________________________# __________

NAME ______________________________________________# __________

Part I)

DTMF Detection using the Goertzel’s Algorithm

Design a MATLAB environment, including a Graphical User Interface, for DTMF detection using the Goertzel’s Algorithm.

- First define synthetic DTMF tones. These tones should be able to dial a phone.

- Your MATLAB detector should be able to detect these synthetic tones under the presence of different levels of additive white noise.

- Your MATLAB detector should be able to detect actual DTMF tones recorded from different phones under different, real-world, noise conditions and interference.

- Your MATLAB detector should be able to meet at least three of the Bell Core Standards.

- Your report should mention and explain performance requirements for:

Minimum accept level, maximum accept level, reject level, twist, frequency accept-reject bands, signal duration, interdigit time, cycle time, echo, DTMF non-linear distortion, presence of dial tone, message circuit noise, impulse noise, speech immunity, adaptive sensitivity.

- Do a literature search on the subject of DTMF detection and include it in your report.

Note: You can monitor the DTMF signals in real time, for up to 10 minutes at a time, using the shareware spectrogram “Gram”.

Spectrogram Web Page: www.visualizationsoftware.com/gram.html

Part II)

Describe your schedule (number of discussion sessions, hours spent at the computer, etc) and your team organizational approach to solve this problem.

Provide a formal report including conclusions (English or Spanish). The report should also include a diskette with a commented m-file that demonstrates your results.

The report will be part of your student portfolio for this course.

References

The copies of four reference papers are available at the DSP lab.